## Slide 1: Exploring Spatial Patterns in Sustainable Integrated Districts: A Methodology for Early-Phase Urban Network Analysis
Anjanaa Devi Srikanth, Srilalitha Gopalakrishnan, Chirag Hablani, Thomas Schroepfer
Published at 2022 Annual Modeling and Simulation Conference (ANNSIM)
Team-06
22241038 S M Rakib Hasan
RA-Md Humaion Kabir Mehedi
ST-Farah Binta Haque

## Slide 2
Introduction and Previous Work
The paper is about exploring spatial patterns in sustainable integrated districts using social network analysis based on graph theory
It is motivated by the need to understand how the spatial configuration of urban districts affects their sustainability and livability
It aims to propose a new methodology for early-phase analysis of large urban spatial networks using two social network analysis methods: Space Syntax and SNAMUTS(Spatial Network Analysis for Multi-modal Urban Transport)
The study also hypothesizes that social network analysis can reveal the spatial patterns and characteristics of urban districts that influence their performance and potential for integration
Previous Works
The paper reviews the literature on urban network analysis, which is a branch of urban studies that uses network theory and methods to analyze urban systems
It identifies two main approaches to urban network analysis: topological and multimodal
It discusses the advantages and disadvantages of each approach and their applications to urban planning and design
The research highlights the gap in the literature on integrating both approaches to capture pedestrian movement patterns more comprehensively

## Slide 3
Scopes of this Study
The findings of this paper can be implemented in-
It addresses the research gap by introducing a new methodology that combines both topological and multimodal approaches to urban network analysis
The study argues that this methodology can provide a more holistic and nuanced understanding of urban spatial networks and their impacts on urban sustainability and livability
It also argues that this methodology can support early-phase decision making and design interventions for sustainable integrated districts
It defines sustainable integrated districts as urban districts that aim to achieve environmental, social, and economic sustainability through spatial integration

## Slide 4
Dataset Description
The datasets used in this paper are:
The paper uses spatial data from various sources, such as OpenStreetMap, Google Maps API, and Singapore Land Authority, which contain information on the land use, street network, building footprint, green space, and public transport network for one-north
It also preprocesses and cleans the spatial data using GIS software and Python scripts to ensure data quality and consistency
The paper divides one-north into 16 subzones based on administrative boundaries and land use characteristics
The study selects four subzones as representative samples for detailed analysis: Biopolis, Fusionopolis, Mediapolis, and Vista Xchange

## Slide 5
Methodology
The paper creates two spatial network models for one-north: one based on Space Syntax and one based on SNAMUTS
The Space Syntax model uses axial lines to represent the connectivity and accessibility of urban spaces. The axial lines are generated using Depthmap software based on an algorithm that minimizes the number of lines needed to cover all street segments in one-north. The axial lines are then assigned weights based on their length and angle.
The SNAMUTS model uses nodes and links to represent the hierarchy and diversity of urban transport modes. The nodes are generated using Google Maps API based on the locations of public transport stops in one-north. The links are generated using Python scripts based on the shortest paths between nodes using different transport modes. The links are then assigned weights based on their distance, travel time, cost, and mode preference.
Both models are converted into adjacency matrices using Python scripts to facilitate social network analysis calculations

## Slide 6
Results
Two methods, OD(Origin-Destination) Matrix and IN-Adjacency(Immediate Neighbor), were used to analyze pedestrian flows in one-north.
The OD Matrix method showed significantly higher node degrees within a 400m radius compared to the IN-Adjacency method, indicating it captures more pedestrian connections.
IN-Adjacency method highlighted road intersections as critical connectors, which did not align with observations.
Certain nodes like Connexis, Galaxis Food Court, one-north Park South, and Fusionopolis Plaza were key connectors in the IN graph but not in the OD graph.
The OD graph displayed higher closeness centrality values for most nodes, reflecting pedestrian behavior more efficiently.
The OD Matrix method was deemed better suited for studying one-north's pedestrian movement.
Both methods revealed dense mixed-use clusters at Fusionopolis, Biopolis, and Mediapolis, which were selected for further spatial network analysis.

## Slide 7
Limitations and Future Research Scope
Limitations:
The paper uses static spatial data that may not match the dynamic urban networks. The spatial data may have errors, changes, or variations that affect the analysis quality and reliability.
It assumes a linear link between SNA metrics and urban performance without other factors. The SNA metrics may have complex or diverse effects on urban performance depending on the context, objectives, or other factors.
Future Research Scopes:
A future scope is to use more dynamic or diverse spatial data, such as from mobile phone or GPS tracking, which can provide more realistic and timely information on urban networks and behavior
A future scope is also to include other spatial indicators, such as density, diversity, or efficiency, which can capture more aspects of urban sustainability and livability

## Slide 8
Conclusion
The paper concludes that the SNA methodology can reveal the spatial patterns and characteristics of one-north that influence its sustainability and livability
It finds that one-north has a high degree of connectivity and accessibility within its subzones but a low degree of integration across its subzones
It also finds that one-north has a high diversity of land use and transport modes but a low hierarchy of transport modes
Finally, It suggests that urban planners and designers can use this methodology and findings to inform spatial planning and design interventions that can enhance the integration and performance of one-north