## Slide 1: How the Urban Microclimate and Outdoor Thermal Comfort Can Affect Intra-City Mobility Patterns: Evidence from New York City
Yang Yang, Desai Wang, Timur Dogan
Published at 2022 Annual Modeling and Simulation Conference (ANNSIM)
Presented By-
22241038 S M Rakib Hasan

## Slide 2
Introduction & Previous Works
Transportation sector's role in U.S. greenhouse gas emissions is the most, with passenger cars as the primary source (US EPA 2022). Recognition of the crucial role of urban planning and design in reducing private vehicle use and promoting active mobility for achieving carbon-free cities, emphasizing the need to consider how the built environment influences travel behavior.
Uses the combination of travel data, built environment data, and Universal Thermal Climate Index (UTCI) calculations for New York City.
Proposes a modeling approach that looks at how travel habits and the built environment are related via the perspective of urban microclimates.
PREVIOUS WORKS
Ewing and Cervero 2010 (Built Environment Impacts): Extensively examines the effects of built environment variables, such as density, land use diversity, and accessibility to urban services, on daily travel choices.
Fu, Lam, and Meng 2014, Koetse and Rietveld 2009, Singhal, Kamga, and Yazici 2014 (Climate-Related Travel Studies): Most climate-related travel behavioral studies focus on the influence of adverse weather events, like heavy rain or snow, on travel behavior. However, the collective impact of microclimate on transportation systems affects individuals' travel patterns over years.
ENVI-met (Bruse 2004) and Eddy3d (Kastner and Dogan 2022) - UTCI Simulation Tools: High-fidelity UTCI simulations are increasingly accessible through advanced tools like ENVI-met and Eddy3d. These tools aid in understanding microclimate impacts on human comfort at a local level.
Although there have been significant works, a huge research gap still exists in this field.

## Slide 3
Research Gap
This paper addresses the following research gaps of the previous studies:
Limited Spatial Scale in Previous Studies: Existing studies linking Universal Thermal Comfort Index (UTCI) with active travel behaviors have predominantly been conducted at a small spatial scale, such as public plazas or specific bike routes. This limitation means that the insights gained are often localized and may not be representative of broader urban contexts.
Computational Challenges: While high-fidelity UTCI simulations are becoming more accessible with advanced tools, they can still be computationally expensive, especially when applied at a city-wide scale. This computational challenge has hindered the comprehensive analysis of microclimate impacts across larger urban areas.
Spatial Heterogeneity: Microclimate impacts can vary significantly across different geographical locations within a city. Current research lacks an in-depth understanding of how microclimate influences travel behaviors in different urban contexts, and capturing this spatial heterogeneity remains a challenge.
Area-Level Metrics: The development of area-level metrics for UTCI is an area where further research is needed. Existing analyses often focus on point-level or street-level data, whereas understanding area-level thermal comfort and its impact on travel patterns is essential for broader urban planning and design interventions.
Lack of Comprehensive Models: While some research has explored the relationship between microclimate and travel, there is a gap in the development of comprehensive models that can predict and quantify the impact of microclimate on intra-city mobility patterns at a larger scale.
Guidance for Urban Design Practices: Another research gap is the development of models that can guide urban design practices. How the insights gained from microclimate research can inform and influence future urban design decisions is an area that requires further exploration.

## Slide 4
Scopes of this Study
The findings of this paper can be implemented in-
Urban Planning and Design: Planners and designers can use this research to create urban environments that are more comfortable and conducive to active travel modes, such as walking and biking.
Decarbonizing Urban Mobility: The study emphasizes the role of active travel modes in reducing greenhouse gas emissions. Policymakers can use this information to develop strategies for decarbonizing urban mobility.
Spatial Planning and Design Interventions: This knowledge of the impact of microclimates on travel behavior can inform decision-making related to spatial planning and design interventions that take into account the thermal comfort of urban residents.
Infrastructure Investment: Understanding the impact of microclimates on travel patterns can influence infrastructure investments. Cities can allocate resources to improve urban environments, making them more suitable for active travel.
Climate-Responsive Urban Design: Climate-resilient and responsive urban design can use the findings to create more comfortable and sustainable urban spaces. This may include the design of shaded pedestrian areas, bike lanes, and green infrastructure.
Transportation Policies: Transportation policies can be adjusted to encourage and facilitate active travel. This may involve creating incentives for walking and biking or designing public transportation systems that integrate with these modes of travel.
Research and Modeling: Researchers and urban scientists can build upon this study to further investigate the relationships between microclimates, built environments, and travel patterns in different cities and regions.

## Slide 5
Dataset Description
The datasets used in this paper are:
Travel Data:
Contains traveler demographic information, including age, income, and household size.
Provides details about trip origin, timestamp, season, time of day, and trip mode.
Includes data on starting and destination activities, trip count, and trip duration.
Built Environment Data:
Offers information on urban density, such as population per square kilometer.
Describes accessibility to various urban services within neighborhoods, including retail, recreational, food, and more.
Data is matched to trip origins, enabling the analysis of built environment impacts on travel behavior.
UTCI Data:
Provides data on Universal Thermal Comfort Index (UTCI) features for neighborhoods and timestamps.
Includes percentages of heat-stress and cold-stress probe points in different areas at specific times.
Enables the study of microclimate's influence on travel behavior and choice of active travel modes.

## Slide 6
Methodology
Modeling framework comprises two main steps: traveler clustering and predictive model training.
Traveler Clustering:
Predictive models estimate traveler preferences, considering mode choice and seasonality.
K-Means clustering performed on combined datasets.
Predictive Model Training:
Random Forest classifier used for outputting trip mode-duration probabilities and Trained through a five-fold cross-validation process for goodness-of-fit evaluation.
L1-norm measures the fit quality of the model.
Spatial Heterogeneity Analysis and Scenario Testing:
Synthetic traveler population generated for each neighborhood based on cluster distribution and predictions made for city-wide active trip percentages using existing features.
Scenario testing explores changes in active trips under hypothetical conditions.
Sensitivity Analysis:
Sensitivity analysis examines UTCI impacts on travel behaviors and explores interdependencies among built environment, microclimate, and travel.
Analyzes various feature combinations in different seasons, times of day, and activities.

## Slide 7
Results
Traveler Clustering and Predictive Model Training Result:
Six traveler clusters successfully derived.
Elbow criterion used for cluster selection, and L1 Norm indicates good model performance.
Spatial Heterogeneity Analysis and Scenario Testing Result:
Active trip proportions based on existing urban context, with higher active trips in Manhattan.
Scenario testing results show increased active trips, especially in work commute trips in specific neighborhoods.
Mode shifts between active and transit modes observed in high-density neighborhoods under varying microclimate conditions.
Sensitivity Analysis Result:
Sensitivity analysis assesses UTCI impact on trip mode and duration.
High-density neighborhoods experience mode shifts between active and transit modes with changes in microclimate.
Changes in trip duration distributions are observed, with more short active trips in high-density areas due to greater destination availability.

## Slide 8
Limitations and Future Research Scope
Limitations:
The study simplifies the modeling by excluding complex microclimate and built environment factors like urban heat islands, wind environments, and human metabolic rate.
The model's accuracy is only assessed through cross-validation and lacks validation against external data sources.
Other mobility data sources, such as GPS or social media, might not provide complete validation data.
Future Research Scopes:
Investigating the impacts of more complex microclimate and built environment factors such as urban heat islands, wind environments, and building surface materials.
Validating the model against external datasets and sources to enhance its accuracy and robustness.
Exploring how other commonly used mobility data sources, like GPS or social media data, can complement and enhance travel behavior models.
Extending the framework to other cities and regions to gain a broader understanding of the relationship between microclimate, built environment, and travel behavior.
Evaluating the effectiveness of microclimate-oriented design interventions in different regions and times for enhanced urban planning and design.

## Slide 9
Conclusion
This research introduces a novel framework that combines travel data, built environment data, and UTCI data to predict neighborhood-level travel choices.
UTCI features can influence up to a 4% change in active trip percentages in dense urban areas.
Dense urban districts, with accessible services and well-shaded streets, are conducive to sustainable travel modes and can support improved thermal comfort.
Active trips are more likely to shift to transit trips in high-density neighborhoods when thermal comfort worsens, which is more environmentally sustainable.